BE77 Spark plug change procedure

tools:
- degreaser
- (AN4027-1) 18mm copper spark plug gaskets ($0.36/each)
- adjustable wrench OR ⅝” wrench
- torque wrench (30-35 ft-lbs / 420 lb-in)
- ⅞” deep socket
- spark plug anti-seize
- gap feeler gauge

Spark plug change procedure:
- disconnect battery
- open cowling
- for each spark plug, one by one
  - loosen wire with adjustable wrench
  - with ⅞” spark plug socket, carefully unscrew plug
  - clean spark plug with pick and degreaser.
  - check gap to about 0.020”
  - lubricate spark plug outer threads with anti-seize
  - lubricate electrical parts with dielectric grease
  - install new copper gasket
  - screw spark plug back in carefully by hand
  - torque to 30 ft lbs
  - connect wire
- runup test
- update maintenance log

Spark plug type:	CHAMPION REM37BY (~$29)

NOTE: Spark plug gage must be set at .016-.022 inch. Installation torque for all spark plugs is 420 inch-pounds (35 foot-pounds). Installation torque for 5/8-24 lead nuts is 80-90 inch-pounds and 110-120 inch-pounds for 3/4-20 lead nuts. Always use new gaskets (P/N STD-295) when reinstalling spark plugs.
Reference: Lycoming Service Instruction No. 1042Z
Example Log entry:

DATE:	November 15, 2014	TACH TIME: 2623.99	SMOH: 559.19
A/C Reg:	N610WM	Model:BE-77	S/N: WA-64
Engine:	Lycoming O-235-L2C	S/N: L-20428-15
Cleaned and measured gap on all spark plugs i.a.w. Lycoming Service Instruction No. 1042Z.
Peter D. Ungsunan
Owner / Pilot 3198409